## Slide 1
The escort demo at a glance
Seen from above. Everything here is decided live; nothing is a recorded routine.
tracked area (the arena)
The VIP
A larger DJI drone, flown by hand by a pilot. It is the thing being protected.
Three defenders
Hold a ring 1 m around the VIP. When a threat comes, the whole ring turns so one defender is in the way.
One attacker
Tries to reach the VIP by hunting for gaps in the ring. It improvises; no two runs are the same.
Cameras and one laptop
Cameras on the walls see every drone 50 times a second. One laptop decides for all of them.

## Slide 2
How the pieces connect
Positions flow in from the cameras; commands flow out over one radio.
Motion-capture cameras
+ the Motive PC
OptiTrack cameras on the walls track reflective markers.
VIP: DJI, hand-flown
tracked like any other drone
The laptop (ROS 2)
positions
50×/s
Mocap receiver
motion_capture_tracking
turns camera data into positions
Escort show
escort_show
decides where every drone should be
Drone server
crazyflie_server
owns the radio, talks to the drones
Crazyradio
USB radio dongle
commands
20×/s each
Crazyflie drones
3 defenders + 1 attacker
~30 g each
Operator presses Enter at each stage

## Slide 3
One decision, 20 times a second
Each step answers one question, and each can be changed without touching the others.
SENSE
Where is everything?
cameras, 50×/s
DECIDE
Is there a threat?
Who blocks it?
escort controller
FORMATION
Where should each
defender be?
the turning ring
SAFETY CHECK
Is that command
allowed?
speed, spacing, room
ACT
Send it to
the drones
radio, 20×/s each
the drones move, and the cameras see it
The safety check does not care how the ring was chosen. That is what lets one offline checker (plan_escort) test the whole chain before anything flies.

## Slide 4
Turn the ring, never swap drones
The drones cannot see each other, so the paths themselves must never cross.
✕
Swap places (not used)
Two drones cross paths right next to the VIP.
✓
Turn the whole ring (what we do)
Every drone moves the same way round. Order never changes.

## Slide 5
Resting ring vs. blocking wall
When the attacker comes close, one defender moves onto its line and the other two close up beside it.
At rest
gap 1.73 m
Three drones 120° apart: big gaps, but nothing to block yet.
Blocking
blocker
wing
wing
Blocker (white light) on the line; wings (violet) close the gaps.

## Slide 6
When does the ring start blocking?
Two distances, not one, so the ring cannot flicker between modes. Drawn to scale.
Ring, 1.0 m
Where the defenders fly.
Alert line, 2.10 m
Attacker crosses inside: blocking STARTS.
Release line, 2.22 m
Attacker must get back out past this before blocking STOPS.
Why so far out? The ring needs a few seconds to turn, so it has to start while the attacker is still out of reach. It was moved out after a test where the attacker got through.

## Slide 7
The speed budget
Every defender is capped at 0.6 m/s. Turning the ring and following the VIP share that one budget.
Ring resting
turning the ring 0.30 m/s
following the VIP 0.30 m/s
Ring blocking
turning the ring 0.55 m/s
0.05
limit 0.60 m/s
While blocking, only 0.05 m/s is left for following the VIP. So the pilot is briefed to hold the DJI still while the attacker is pressing. Small drifts before and after are fine.
To give the VIP more room you must turn the ring more slowly, shrink the ring, or let the drones fly faster near people. Each has a cost.

## Slide 8
Why the defenders can win: the inside track
Both sides race for the same direction around the VIP. The defenders run the shorter circle.
defenders: 1.0 m from VIP
attacker held ~1.8 m out
Same angle, shorter trip.
To swing the same angle around the VIP, the attacker has to fly about 1.8× further than a defender.
0.55 rad/s
how fast the ring may turn while blocking
0.33 rad/s
how fast the attacker can circle at its 0.6 m/s limit
~1.0 m/s
attacker speed at which it would start to win
The attacker is no faster than a defender (both are capped at 0.6 m/s). The defenders win on geometry, not on speed.

## Slide 9
Layers of safety
No single check is trusted. Each layer catches what the one before it can miss.
Before take-off
can still be fixed by moving a drone
plan_escort checks the whole plan fits the room and keeps every distance
the take-off paths are checked for near misses
every drone is tracked, on its floor mark, and able to arm
In flight, every 1/20 s
automatic
every command is limited in speed, spacing and room
each drone’s REAL position is watched: lost tracking → hold, then land
VIP lost → the ring holds, then lands
VIP flown out of its box → the ring parks (cyan) and waits
Ways out
a human decides
Ctrl-C or Abort: stop, land, switch off. A controlled landing.
E-STOP: motors off instantly. The drones drop. Needs a battery re-plug after.

## Slide 10
The show, step by step
Operator-paced: nothing advances until someone presses Enter. The defence never waits.
0
Checks
Placement, tracking and arming are verified.
Enter: arm
1
Take off
Drones lift and form the ring, parked high for the DJI.
amber
automatic
2
DJI up
Pilot flies the DJI up under the ring. Ring locks on.
pilot, then Enter
3
Station
Attacker moves to one side, sizing up the ring.
amber
Enter
4
Attack
Attacker hunts the gaps. Ring turns to block.
red
Enter
5
Stand down
Attacker gives up and withdraws.
magenta
Enter
6
DJI down
Ring climbs clear. Pilot lands the DJI.
amber
pilot, then Enter
7
Land
All four drones land and switch off.
automatic
Lights: the attacker’s colour, except steps 1 and 6 where ALL drones go amber ("your move"). With a fixed point as the VIP (no DJI), steps 2 and 6 are skipped. Ctrl-C, Abort or q lands everything at any step.

## Slide 11
What the lights mean
Colours are status, not decoration. Each colour has exactly one meaning.
Red
the attacker, pressing
Amber
attacker taking station, or ALL drones: waiting for a human
Magenta
the attacker has stood down
White
the defender currently blocking
Violet
the two wings, closed up beside the blocker
Deep blue
the resting ring, nothing to do
Cyan
all 3 defenders: the VIP left its box, the ring is parked and waiting
If the defenders all turn cyan, fly the DJI back toward the middle of the arena. They resume on their own.
Before and after the show: green = connected and ready, red = a script is in control.

## Slide 12
Flight day, in order
Do the simulator once first. Skipping a step is how the known accidents happened.
1
Check plan
no drones needed
plan_escort
2
Place drones
on their floor marks
place_drones.py
3
Record marks
yaml = where they ARE
sync_initial_positions
4
Radio scan
every drone must answer
scan_fleet.sh
5
Launch
mocap, server, GUIs
ros2 launch crazyflie launch.py
6
Preflight GUI
go / no-go per drone
battery, mocap, yaw
7
Dry run
checks, arms nothing
dry_run:=true
8
Fly
operator-paced
escort_show
Steps 2–3 run with mocap up but NO server (server:=False): nothing owns the radio, nothing can arm.

## Slide 13
The safety filter: every command, every tick
Three stages in a fixed order. The last rule applied always holds, so the order is the priority.
desired
target
1 SLEW
limit acceleration,
then speed
2 SEPARATIONS
push the point out of each
keep-out circle, a few passes
3 ROOM
pull the point back inside
the arena and height band
sent to
the drone
Inside stage 2, order matters:
away from the attacker
away from the other defenders
away from the VIP: LAST, so it always wins
Slew first, then separations. The other way round, the slew drags the drone straight back inside the limit (a real bug in an early version).

## Slide 14
Two ways to command a Crazyflie
The escort uses both, and hands over between them.
High-level commands
takeoff, goTo, land
One goal and a duration. The DRONE plans a smooth path and flies it on its own.
Used for: take-off, forming the ring, landing.
Streaming
cmdFullState
A new position + velocity every 1/20 s. The LAPTOP plans; it must keep sending.
Used for: the escort itself, which reacts to things that move.
first streamed setpoint takes over;
notifySetpointsStop hands back
If streaming stops: after 0.5 s the drone levels out; after 2 s its motors stop and it falls (then needs a battery re-plug). So every code path, including waiting for a human, keeps sending.

## Slide 15
The reactive attacker
Pulled toward the widest gap, pushed away by defenders and walls. Hard limits are enforced separately.
STATION
wait off to one side
Enter
ATTACK
hunt the widest gap
Enter, or
it gives up
STAND DOWN
withdraw to station
Gap seeking
Aims at the widest gap between defenders, preferring gaps away from where it is, so it flanks. Commits to a gap until a defender closes it.
Giving up
Remembers its closest approach. If it cannot beat that for a while, it stands down on its own.
Hard limits
Forces only make it LOOK careful. After every step its point is pushed out of a keep-out circle round the VIP and round each defender.
Same speed as a defender
It plans at 0.8 m/s, but its commands go through the same safety filter, so it flies at 0.6 m/s at most.

## Slide 16
Inside one controller step
What escort.py does every 1/20 s, from positions in to commands out.
Positions in
VIP, attacker, defenders
VIP velocity
smoothed estimate
Blocking?
alert / release latch
Pick the blocker
slot nearest the threat,
with a margin
Turn the ring
at a limited rate
Close the wall
blend wings in or out
Slot targets
VIP + 1 m at each angle
Sanity gate
ignore a pose that is
implausibly far off
Safety filter
per drone
Commands out
position + velocity
On release the ring HOLDS its angle instead of turning back home; winding back made it oscillate with the attacker.

## Slide 17
One control tick, end to end
Who talks to whom in 1/20 s. Arrows down the page are time.
Mocap
/poses
escort_show
laptop
crazyflie_server
laptop
Crazyflie
firmware
latest poses (cached, 50 Hz)
same poses
poses → onboard estimator
cmd_full_state × 4 drones
radio: position + velocity
checks, attacker model,
controller step, safety filter
drone’s own controller
tracks the setpoint
wait for the next tick,
still handling messages

## Slide 18
How it is checked before it flies
The checker runs the SAME controller code as the flight script. Only the drones are simulated.
plan_escort
pure Python, seconds
same controller objects;
drones modelled as a simple lag
Simulator
full ROS stack
real show script, simulated
drones (no mocap)
Hardware, in stages
one change at a time
fixed point → DJI →
attacker
What a pass means
Every distance, speed, room limit and altitude held for a whole simulated encounter, AND the ring stayed a ring.
Sweeps
Find the limit, e.g. the fastest VIP walk at which everything still holds.
Honest limits
The drone model is assumed, not measured. The simulator publishes no mocap, so position handling is first tested on hardware.

## Slide 19
Design lessons that carry over
Geometry over tuning
Rotate, never swap. The nearest slot leads. The inside track wins.
Projections over forces
Hard limits are projections. The last one applied wins, so order is priority.
Hysteresis everywhere
Engage/release, blocker hand-over, gap choice, geofence re-entry.
Check the drone, not the command
Watch real positions and tracking error; ignore implausible measurements.
Never block the loop
Waiting for a human still streams. Humans pace the attacker, never the defence.
One source of truth
The checker runs the flight code. The room lives in one file. Directions rotate with the frame.

## Slide 20
The lab network
Only the laptop ↔ Motive link uses the network. The drones never join it: they use the radio.
OptiTrack cameras
up to 240 Hz
LAN cable
Mocap router
cameras only
LAN cable
Motive PC (Windows)
streams NatNet multicast, 50 Hz
Hangar switch
wired
Lab router
5 GHz Wi-Fi, same subnet as Motive
positions
(wired)
Laptop
ROS 2, the escort show
Wi-Fi
or cable
Crazyradio
Changing the laptop from Wi-Fi to cable (or back) changes the Motive address. Leave hostname: "auto" in motion_capture.yaml and the launch finds Motive by itself.

## Slide 21
Strike and guard: one problem, two demos
Small drones with no sensors of their own, guarding something against attackers.
Escort
guard a moving VIP
Team
3 defenders, 1 attacker (4 drones)
Guards
a hand-flown DJI that moves
Control
reacts to the cameras 20 times a second
Checked
every command, live, before it is sent
Status
flown for guests, 8 Oct 2026
STL game
guard a goal line
Team
5 defenders, 5 intruders (10 drones, 2 radios)
Guards
five goals on one edge of the square
Control
the whole flight is planned before take-off
Checked
every moment of the planned flight, before arming
Status
simulator only with this repo's show
Shared: the same cameras, radio, server, safety code (abort, preflight, room limits) and flight-day routine.

## Slide 22
The STL game at a glance
Seen from above. Intruders cross the square to their goals; defenders try to stop them.
game square, 4 m × 4 m
Five intruders
Start on the left. Each heads for its own goal on the right edge, dodging and faking.
Five defenders
Start near the goal line. Each is matched to an intruder, the most urgent first.
Goals
An intruder that reaches its goal scores (REACHED).
Blocked
An intruder a defender pins in place is BLOCKED and lands at once.

## Slide 23
Plan the whole flight, then fly it
The game never reads the cameras while it plays, so one number (the seed) fixes the flight.
1 SEED
one number, printed
every run
2 PLAY
the laptop plays the
whole game (~1 s)
3 CHECK
every moment: spacing,
speed, start move
4 FLY
send exactly the moves
that were checked
refuses to arm if any check fails
Escort: reacts to the cameras live; checks each command as it is sent
STL game: plays the game in advance; checks the whole flight before arming
Same seed, same flight: seed:=N replays a run, and plan_stl --seed N checks it offline.

## Slide 24
The STL flight, step by step
No prompts: once armed, the game runs to the end. Ctrl-C lands all ten at any time.
0
Checks
Plan checked for the seed; tracking, marks and arming verified.
before arming
1
Take off
All ten lift to 0.3 m.
3 s
2
Start move
Climb to 1.0 m and move to the start slots.
3 s
3
Game
Intruders run for their goals; defenders block. A blocked intruder lands at once.
~10 s
4
Intruders land
Any intruder still flying lands.
5 s
5
Return
Defenders fly back to their start slots.
~4 s
6
Land
Defenders land and everything disarms.
5 s
About 30 seconds from take-off to landing. Every run prints its seed and the closest approach planned.

## Slide 25
What the lights mean in the STL game
Set by the game itself, so they show what the plan says is happening.
Blue
a defender
Magenta
an intruder still in play
Red
an intruder that was BLOCKED (it lands)
Green
an intruder that REACHED its goal
Green also means "connected and ready" before and after a show, on every demo. During the STL game it means an intruder scored. That is the original script's choice.
The escort uses a different set of colours: see its own light legend.